| Short Overview 1-axis, active solar tracker total module surface max. 10 m2, approx. 1.6 kWp maintenance-free high reliability and life expectancy no failure prone light sensor low power consumption, approx. 1.25 kWh per year no unnecessary tracking movements designed to withstand wind speeds up to 150 km/h cost-efficient tracking system 2 years manufacturer's warranty against defects in material and workmanship |  | Applications Single-axis solar tracking increases the energy return of solar modules, dependent on location, by 25% (e.g. Germany) up to 40% (e.g. central US, Korea, Spain) per year in average, respectively up to 55% during the summer months. Use e.g. for remote homes livestock plantation irrigation pool filtration solar heating etc. |
| --- | --- | --- |

| Features extremely reliable active tracking system angle East-West: 90o, active elevation angle: 0o - 45o, manually adjustable no separate sensors, it uses the modules as sensor energy supply of tracking drive: 12 V nominal, max. 200 V (Voc) provided by one of the tracked modules horizontal position at night tracking in steps according to the daily sunshine duration designed to withstand wind speeds up to 150 km/h Note Tracked PV systems for charging batteries require a small extra PV-module: min. 12 V (nominal), max. 200 V (Voc) for latitudes above 45o North: min. 10 Wp for latitudes below 45o North: min. 5 Wp |  | Module Surface and Fixation 10 m2 total module surface (up to 1.6 kWp, dependent on module type) fixation: stainless steel clips, fitting for most module types - no drilling of additional holes into the module frame |
| --- | --- | --- |

| Included in Delivery frame and fixation elements made of steel, Zn coated stainless steel clips for modules electronics incl. battery in plastic housing linear motor mounting pole DIY System Do It Yourself and cut cost with the DIY kit includes all fixation elements made of ZN coated-steel, stainless steel clips for modules, ETATRACK Control and a heavy duty linear drive included. TWIN System one Controller operates two trackers DIY Kits available |  | Mounting Pipe Requirement mounting pole: 2.5 m surface concrete foundation (approx. 1.6 m3) Packing Dimensions 4 boxes each 255 x 17 x 17 cm total weight: 320 kg total volume: 0.3 m3 |
| --- | --- | --- |