| Short Overview 1-axis, active solar tracker total module surface max. 4 m2, approx. 500 Wp maintenance-free high reliability and life expectancy no failure prone light sensor low power consumption, approx. 1.25 kWh per year no unnecessary tracking movements designed to withstand wind speeds up to 120 km/h cost-efficient tracking system 2 years manufacturer's warranty against defects in material and workmanship |  | Applications Single-axis solar tracking increases the energy return of solar modules, dependent on location, by 25% (e.g. Germany) up to 40% (e.g. central US, Korea, Spain) per year in average, respectively up to 55% during the summer months. Use e.g. for remote homes livestock plantation irrigation pool filtration solar heating etc. |
| --- | --- | --- |

| Features extremely reliable active tracking system angle East-West: 90o, active elevation angle: 0o - 45o, manually adjustable no separate sensors, it uses the modules as sensor energy supply of tracking drive: 12 V nominal, max. 200 V (Voc) provided by one of the tracked modules horizontal position at night tracking in steps according to the daily sunshine duration designed to withstand wind speeds up to 120 km/h Note Tracked PV systems for charging batteries require a small extra PV-module: min. 12 V (nominal), max. 200 V (Voc) for latitudes above 45o North: min. 10 Wp for latitudes below 45o North: min. 5 Wp |  | Module Surface and Fixation 4 m2 total module surface (up to 500 Wp, dependent on module type) fixation: stainless steel clips, fitting for most module types - no drilling of additional holes into the module frame |
| --- | --- | --- |

Mounting and Packing

| Included in Delivery frame and fixation elements made of steel, Zn coated stainless steel clips for modules electronics incl. battery in plastic housing linear motor mounting pole not included in delivery |  | Mounting Pipe Requirement mounting pole: 2 m surface concrete foundation (approx. 0.7 m3) Packing Dimensions 1200 x 400 x 160 mm total volume: 0.08 m3 total weight: 44 kg |
| --- | --- | --- |

Fitting Modules

Selection of fitting modules. For other module types, please check dimensions drawing in the product information (PDF, 34 kB).

| Type of PV Module | Quantity of PV Modules | max. Wp |
| --- | --- | --- |
| Astropower AP 110 | 4 | 440 |
| BP 3125 | 4 | 500 |
| BP 3160 | 3 | 480 |
| BP 380 | 5 | 400 |
| GE 165 | 3 | 495 |
| GE 173 | 3 | 519 |
| Isofoton I 110 | 4 | 440 |
| Kyocera KC 125 | 4 | 500 |
| Sharp 123 Wp | 4 | 492 |
| Sharp 80 Wp | 5 | 400 |
| Shell 85 Wp | 5 | 425 |
| Shell SQ150C | 3 | 450 |