| Overview lift up to 240 m flow rate up to 11 m3/h simple installation maintenance-free high reliability and life expectancy cost-efficient pumping 2 years manufacturer's warranty against defects in material and workmanship |  | Applications drinking water supply livestock watering pond management irrigation etc. |
| --- | --- | --- |

Performance

PS1200 HR-03 HR-03H HR-04 HR-04H article # 1228-X 1230-X 1235-X 1240-X lift [m] 0-140 140-240 0-80 80-160 max. flow rate [m3/h] 0.5 0.5 0.8 0.8 max. efficiency [%] 60 64 60 65 solar operation nominal voltage 72-96 V DC open circuit voltage max. 200 V DC solar generator [Wp] 350-480 420-900 350-420 420-1200 battery operation nominal voltage 72-96 V DC PS1200 HR-07 HR-10 HR-14 HR-20 article # 1245-X 1250-X 1255-X 1260-X lift [m] 40-120 30-80 0-60 0-40 max. flow rate [m3/h] 1.2 1.9 2.7 3.6 max. efficiency [%] 64 64 65 64 solar operation nominal voltage 72-96 V DC open circuit voltage max. 200 V DC solar generator [Wp] 420-1200 420-1200 350-1200 480-1200 battery operation nominal voltage 72-96 V DC PS1200 C-BF-04 C-DF-03 article # 1220 1225 lift [m] 0-25 0-15 max. flow rate [m3/h] 7.3 11 max. efficiency [%] 40 40 solar operation nominal voltage 72-96 V DC open circuit voltage max. 200 V DC solar generator [Wp] 350-1200 840-1200 battery operation nominal voltage 72-96 V DC

Features

| Controller PS1200 controlling of the pump system and monitoring of the operating states mounted at surface (no submerged electronic parts) two control inputs for well probe (dry running protection), float or pressure switches, remote control etc. automatic reset 20 minutes after well probe turns pump off protected against reverse polarity, overload and high temperature speed control, max. pump speed adjustable to reduce flow rate to approx. 30 % solar operation: integrated MPPT (Maximum Power Point Tracking) battery operation: low voltage disconnect and restart after battery has recovered max. efficiency 92 % (motor + controller) enclosure: IP 54 (sealed, weatherproof) |  | Motor ECDRIVE 1200 HR / C brushless DC motor water filled dynamic slide bearings, material: carbon/ceramic wetted material: stainless steel (AISI 316), POM, rubber, cable drinking water approved Pump end (PE) high life expectancy none-return valve dry running protection (optional) material: stainless steel (AISI 316), rubber for HR pumps only helical rotor pump (positive displacement pump) two main parts only: stator and rotor stator: geometry made of abrasion resistant rubber rotor: stainless steel, hard chrome plated, abrasion resistant more resistant to damage by sand than other pump types self-cleaning |
| --- | --- | --- |