| Overview lift up to 180 m flow rate up to 11 m3/h simple installation maintenance-free high reliability and life expectancy cost-efficient pumping 2 years manufacturer's warranty against defects in material and workmanship |  | Applications drinking water supply livestock watering pond management irrigation etc. |
| --- | --- | --- |

Performance

| PS600 | HR-03 | HR-03H | HR-04 | HR-04H |
| --- | --- | --- | --- | --- |
| article # | 1040-X | 1045-X | 1050-X | 1055-X |
| lift [m] | 0-140 | 140-180 | 0-80 | 80-140 |
| max. flow rate [m3/h] | 0.5 | 0.5 | 0.8 | 0.8 |
| max. efficiency [%] | 60 | 64 | 60 | 65 |
| solar operation | nominal voltage 48-72 V DC open circuit voltage max. 150 V DC |
| solar generator [Wp] | 300-480 | 420-900 | 300-480 | 420-900 |
| battery operation | nominal voltage 48 V DC |

| PS600 | HR-07 | HR-10 | HR-14 | HR-20 |
| --- | --- | --- | --- | --- |
| article # | 1060-X | 1065-X | 1070-X | 1080-X |
| lift [m] | 40-90 | 30-60 | 0-50 | 0-30 |
| max. flow rate [m3/h] | 1.2 | 1.9 | 2.7 | 3.6 |
| max. efficiency [%] | 64 | 64 | 65 | 64 |
| solar operation | nominal voltage 48-72 V DC open circuit voltage max. 150 V DC |
| solar generator [Wp] | 420-900 | 420-900 | 300-900 | 420-900 |
| battery operation | nominal voltage 48 V DC |

| PS600 | C-BF-04 | C-DF-03 |
| --- | --- | --- |
| article # | 1296-X | 1298-X |
| lift [m] | 0-20 | 0-10 |
| max. flow rate [m3/h] | 7.3 | 11 |
| max. efficiency [%] | 40 | 40 |
| solar operation | nominal voltage 48-72 V DC open circuit voltage max. 150 V DC |
| solar generator [Wp] | 300-900 | 720-900 |
| battery operation | nominal voltage 48 V DC |

Features

| Controller PS600 controlling of the pump system and monitoring of the operating states mounted at surface (no submerged electronic parts) two control inputs for well probe (dry running protection), float or pressure switches, remote control etc. automatic reset 20 minutes after well probe turns pump off protected against reverse polarity, overload and high temperature speed control, max. pump speed adjustable to reduce flow rate to approx. 30 % solar operation: integrated MPPT (Maximum Power Point Tracking) battery operation: low voltage disconnect and restart after battery has recovered max. efficiency 92 % (motor + controller) enclosure: IP 54 (sealed, weatherproof) |  | Motor ECDRIVE 600 HR / C brushless DC motor water filled IP 68, pressure balanced, max. submersion unlimited dynamic slide bearings, material: carbon/ceramic wetted material: stainless steel (AISI 316), POM, rubber, cable drinking water approved Pump end (PE) high life expectancy none-return valve dry running protection (optional) material: stainless steel (AISI 316), rubber for HR pumps only helical rotor pump (positive displacement pump) two main parts only: stator and rotor stator: geometry made of abrasion resistant rubber rotor: stainless steel, hard chrome plated, abrasion resistant more resistant to damage by sand than other pump types self-cleaning |
| --- | --- | --- |